## Slide 1
Mine Principale Rehabilitation and Restoration Plan
Chibougamau, Québec
March 2014

## Slide 2
Table of Contents
  Context and Issues
  Objectives and Approach
  Proposed Scenario per Sector
  Preliminary Work
  Monitoring

## Slide 3
Localisation and Description
Lac aux Dorés
Copper Rand
Chibougamau

## Slide 4
Site Background
Gold mining and milling facilities (~ 50 yrs)
1959

## Slide 5
19 million tons of mining waste in 3 tailings ponds (Tailing sites A, B and C)
1,7 km2 = 50 times the area cover by the Core center of Oujé-Bougoumou
x 50
Site Description

## Slide 6
Failure of Ressources Meston in 2010
No rehabilitation work done
Quebec government decided to act on this abandoned mine site
Site Context

## Slide 7
Mine waste
  Acid mine drainage
    Metals dissolved in water makes the water acid and change color to orange
  Leachable metal contaminants
    Cu, Ni, Zn, Cd, Co, …
Site safety
  Wide underground openings
  Ground stability
General Problematic
Acid mine drainage

## Slide 8
Site safety
Acceptable environmental state
Compatibility with future use
Main Rehabilitation Objectives

## Slide 9
Flight Animation

## Slide 10
Operation Site Issues
OP
Hydrocarbon contamination
(8 010 m3)
Groundwater pumping to avoid Lac aux Dorés contamination
Wide underground openings, site safety and ground stability
Overview

## Slide 11
Tailing Sites A, B and C Issues
LAD
Water seepage through backfill on the shore (Site A)
Occasional overflow of contaminated water
(Site A)
Seepage at the foot of the dykes
(Sites B and C)
Wind erosion
Overview

## Slide 12
Lac aux Dorés water contamination (fish habitat)
Dust emission from tailings
Security of the site
Efficiency and sustainability of the proposed rehabilitation scenarios
Local Communities Issues

## Slide 13
Recreational activities on the lake
Fishing and hunting
Gathering place
Local Communities Future Use

## Slide 14
MRN Restoration Measures
Mitigate the contamination
Assure site safety
Design a solution using a renaturalisation approach
Control wind erosion
Aim for a site compatible with recreational uses, including hunting and fishing

## Slide 15
Technologies to prevent acid generation
  Elevated water table technique combined with a monolayer cover
Available Restoration Technologies

## Slide 16
Technologies to prevent acid generation
  Oxygen barrier cover (HDPE membrane)
Restoration work at Eustis mine : Oxygen barrier cover (2006)
Available Restoration Technologies

## Slide 17
Example of rehabilitation and restoration work (Eustis)
Before
After
Available Restoration Technologies

## Slide 18
Example of rehabilitation and restoration work (Normetal)
Available Restoration Technologies
Before
After
Before

## Slide 19
Example of rehabilitation and restoration work (Poirier)
Available Restoration Technologies
Before
After

## Slide 20
Available Restoration Technologies
Solutions and technologies to treat contamined soil with hydrocarbons
  Excavation and treatment on site
Air
Water
Impermeable cover
Contamined soil
Air and liquid treatment unit
Clean liquid
Clean air
Impermeable slab
bons
Hy
dro
car

## Slide 21
Biopile
Available Restoration Technologies

## Slide 22
Proposed restoration scenarios
OP
To excavate and to treat contaminated soil
To reshape the open-pit slope
Operation site
To stabilize the underground mine openings
To excavate waste rock and to dispose it on sites B and C
To excavate tailings and to dispose them on sites B and C
Overview
To revegetate

## Slide 23
Proposed Restoration Scenario
1. To excavate and to dispose on sites B and C
2. To flood
Tailing site A
3. To revegetate
4. To install a wave breaker
5. To place an erosion protection blanket on the lake shore
A
Before
Overview

## Slide 24
Renaturalisation Approach
To create an environment favorable for plant and wildlife
To create a new bay in order to allow fish to spawn and feed
To design a wave breaker to include 3 nesting areas for geese and waterfowls
Tailing site A

## Slide 25
Future View of Tailing Site A
Before
After

## Slide 26
1. To consolidate and to waterproof the dykes
2. To install impervious walls
Tailing sites B and C
3. To install impervious cover with HDPE
Overview
B
C
Proposed restoration Scenario
4. To install a semi-permeable cover
5. To revegetate
6. To install wind barriers
7. To place an erosion protection blanket

## Slide 27
Renaturalisation Approach
Tailings sites B and C
To install ecological corridors (indigenous vegetation mounds)
To install wind barriers
To favor nesting area for swallows

## Slide 28
Future View of Tailing Sites B and C
After
Before

## Slide 29
Future View of Mine Principale Site
Before
After

## Slide 30
Preliminary Studies and Works
To reopen the bridge prior to work and dismantle the bridge afterwards
Search for nearby borrow material (sand, gravel, etc.)
To assess the impact of contamination from Copper Rand by the middle dyke

## Slide 31
Overall work
Around 150 M$
  Engineering
  Rehabilitation work
    4 phases
  Post-restoration monitoring

## Slide 32
Upcoming steps
Preliminary schedule

## Slide 33
Post-restoration Monitoring
Surface water quality
Underground water quality
Stability and vegetation recovery
Eustis mine
Eustis mine
New Calumet mine

## Slide 34
Participation and communication
  Cree
  Chibougamau
Technical discussions at the Groupe de travail cri (formed after the SMi Presentation of Mine Principale Rehabilitation and Restoration Program on January 22nd 2013)
Meetings with local communities
Approach with the Communities

## Slide 35
Approach with the Communities
Obtain reliable information on the extent mining contamination
Oversee any resulting remediation and restoration activities
Steering Commitee
Cree Board of Health and Social Services of James Bay
Ville de Chibougamau
Eeyou Istchee
Oujé-Bougoumou

## Slide 36
Approach with the Communities
Ville de Chibougamau
Eeyou Istchee
Oujé-Bougoumou
Sub-Committee of the Steering Committee
Rehabilitation and restoration of Mine Principale
Approval of all the work to be done
Technical Commitee

## Slide 37
Overall
MRN objective : get the site back to a natural state
Work done in compliance with communities issues and expected uses of the site
  Collaboration with the communities
  Participation of the communities
  Information of the communities

## Slide 38
Thank you
Any questions ?